## Slide 1: Rapid-Response Defibrillator Drone
ORION UAV Design Challenge | Senior Track | Team 04 PHSS
Saarang A Nair (Team Leader, CAD) · Harsharaj R (CAD)
Pramodh Bala T · Sonit Nooney
11 October 2026
Notes: [0:00-0:10] Introduce team and the mission: get an AED to a cardiac arrest within 5 minutes across a 5 km radius.

## Slide 2: Problem and assumptions
5 km
service radius
5 min
to reach and deliver
2.5 kg
AED payload
≥70 km/h
cruise speed
<25 kg
takeoff weight
The real need
Survival falls roughly 7-10% for each minute without defibrillation
A bystander must use the AED with voice guidance, no training needed
Flying straight over traffic: 5 km takes about 4 min at 80 km/h
Assumptions
Hot day (air density 1.225 kg/m³), rain, no wind in baseline
Dock at the centre of the area; one-way 5 km, then return
BVLOS flights approved by DGCA; AED and case total 2.5 kg
Notes: [0:10-0:30] Problem understanding. The five numbers are the brief. The real need is an AED in a bystander's hands in minutes. Assumptions: hot day, rain penalty of 10% power, dock at centre, BVLOS approval.

## Slide 3: Concept selection: why a hexacopter
 | Hexacopter (selected) | Quadcopter | Hybrid VTOL
Hover and winch precision | High: 6 rotors | Medium | Medium: wing gusts
Motor-out tolerance | Design target: survives 1 | None | Partial
Cruise energy per km | Higher (about 23 Wh/km) | Higher | Lowest
Design and control risk | Low: one flight mode | Low | High: transition
Launch from a small dock | Pad only | Pad only | Pad plus transition
The 5 min target is won by speed and a zero-preflight standby, not by wings. A hexacopter gives maneuverability and hover safety over people and redundancy, and a simpler build within 48 hours.
Notes: [0:30-1:00] We compared a quad, a hexacopter and a hybrid VTOL. VTOL wins on cruise energy but adds transition risk and complexity. A hexacopter hovers steadily for the winch, can tolerate a motor loss as a design target, and is realistic in 48 hours. Cruise energy is higher, so we pay in battery, which we can afford within 25 kg.

## Slide 4: Ready Standby and seamless power transition
Ground station
Dispatch with coordinates
Dock supply
Constant 50.4 V, always on
Power multiplexer
Ideal-diode OR-ing, no reverse current
12S battery
Stays full, unloaded
Avionics + ESC bus
FC, Pi 5, radio live; hold-up cap
Drone: armed standby
GNSS lock, EKF converged
Dispatch to takeoff in seconds
No boot, no GNSS search, no preflight checks. Flight energy is not spent on standby.
Docked: loads run from the dock. On release the battery takes over with no dropout; a hold-up capacitor bridges the switch-over for the flight controller and Pi 5.
Notes: [1:00-1:30] Pre-validated emergency dispatch. The drone sits armed in a monitored standby so no boot, GNSS lock or preflight is needed after dispatch. Standby power comes from the dock through an ideal-diode power mux, so the battery stays full. When the drone leaves the dock, the battery takes over automatically with no interruption.

## Slide 5: Aerodynamic and structural sizing
16.17 kg
takeoff weight
4.43 : 1
max thrust-to-weight
2.1 kW
hover power (electric)
Chart: Mass budget (kg)
| Winch, latch, speaker | AED payload | Airframe and Avionics | Motors, ESCs, props | Battery 12S
Mass (kg) | 1.76 | 2.5 | 4 | 4.74 | 4
Six X6 Plus (24 inch props, IPX6): 3 kg per axis, 25% throttle in hover
Faired body tilts only 8° at 80 km/h; 30 mm carbon-tube arms; sealed avionics bay
Notes: [1:30-2:00] Mass budget totals 18.1 kg, well under 25 kg. Six X6 Plus motors give about 3.9 times thrust-to-weight, so hover sits near a quarter throttle and the vehicle keeps margin for gusts and a motor loss. Drag area is an assumption we would refine in CFD.

## Slide 6: Avionics architecture
Sensors
Dual-antenna RTK GNSS
LiDAR altimeter
Optical flow camera
Load cell on tether
Compute
Pixhawk-standard FC (PX4)
Raspberry Pi 5 companion
uXRCE-DDS bridge
Actuators
6 ESCs (CAN)
Winch controller / relay
Electronic release latch
Voice: MP3 + speaker
Link: 865-867 MHz telemetry (licence-free in India, not 900 MHz) plus 4G backup; loss of both triggers autonomous return.
Notes: [2:00-2:25] Sensors feed a Pixhawk-class flight controller, which keeps the safety-critical loops. The Raspberry Pi 5 handles mission logic through the uXRCE-DDS bridge. Note the telemetry band: 900 MHz is not licence-free in India, so we use 865-867 MHz plus a 4G link.

## Slide 7: Software and algorithm design
STANDBY
DISPATCH
CLIMB
CRUISE
DESCEND
WINCH
RELEASE
RETURN
Navigate
RTK + EKF fusion; geofenced low-risk corridor; speed command trades time against energy
Deliver
Hover within 0.5 m using RTK and LiDAR; damp tether swing; load-cell slack opens the latch
Supervise
Pi 5 monitors link, battery and motors; FC watchdog runs independently and can end the flight
Notes: [2:25-2:55] The mission is a state machine from standby to return. Cruise and winch are the two phases where we spend design effort. Navigation uses RTK and EKF; delivery uses RTK plus LiDAR with swing damping and a load-cell touchdown detect; the Pi 5 supervises while the flight controller keeps an independent watchdog.

## Slide 8: Analysis results
Chart: Power vs airspeed (kW)
| 0 | 30 | 50 | 70 | 80 | 90 | 100
Electric power (kW) | 2.14 | 1.75 | 1.56 | 1.67 | 1.84 | 2.08 | 2.4
Chart: Mission time vs cruise speed (s)
| 70 km/h | 80 km/h | 90 km/h
Mission time (s) | 318 | 286 | 261
At 70 km/h the flight takes 5 min 18 s, so we cruise at 80 km/h: 4 min 46 s
Energy: 225.1 Wh out + 84.5 Hover + 195 Wh back vs 117 Wh usable (18.8% reserve)
Momentum-theory model in Python: density 1.15, figure of merit 0.65, motor+ESC 85%, drag area 0.09 m² (assumed), +10% rain. Not CFD or flight data.
Notes: [2:55-3:25] Results from our analytical sizing model. Power is lowest around 50 km/h and rises with speed. The key finding: the minimum 70 km/h cruise does not meet 5 minutes once takeoff, descent and 30 s of winching are added, so we cruise at 80 km/h with a dash option to 90. Battery capacity is enough for the round trip with large reserve. Be honest that these are model results with assumed drag area, not flight data.

## Slide 9: Safe delivery and termination
Near people
Drone holds at 15 m; AED lowered on a tether at about 0.5 m/s
RTK hover keeps the drop inside the 5 m x 5 m zone
Load cell senses touchdown, then latch releases; weak link frees a snag
Voice and siren announce the descent; operator confirms the zone is clear
Termination over crowds
1
Reroute
Corridor over roads and water
2
Land
Nearest pre-mapped safe site
3
Parachute
Motors cut, independent trigger
Notes: [3:25-4:00] Near people: the drone never lands; it stays at 15 m and lowers the AED on a tether, releases on touchdown, and announces itself by voice. Termination is tiered: reroute along low-risk corridors, land at a safe site, and as last resort cut the motors and deploy a parachute with an independent trigger. Parachute sink rate is an assumption to be sized.

## Slide 10: Feasibility, scalability and cost
Item | INR (k)
Propulsion: 6 x X6 Plus | 95
FC, dual RTK GNSS, Pi 5, sensors | 126
Radio and 4G link | 15
Winch, latch, voice | 59
Battery and frame | 105
Dock and power mux | 90
Wiring and misc | 20
Total (excl. AED) | 510
Indicative estimates; supplier quotes pending.
Scaling up
One dock covers about 79 km²; add docks as a grid
Off-the-shelf parts, carbon tubes, bolt-together frame
Payload bay is swappable: other medical kits
Hybrid VTOL is the upgrade for 10 km and beyond
Notes: [4:00-4:20] Feasibility: all parts are off-the-shelf and the mass and energy close with margin. Cost is about 5.1 lakh rupees excluding the AED, with figures indicative. Scaling: each dock covers about 79 square kilometres, and the payload bay can carry other medical kits.

## Slide 11: Risks, regulation and ethics
Risk | Mitigation
5 min margin is thin | Cruise 80 km/h, dash 90; standby cuts launch delay
Gusts on the tether | RTK hover, swing damping, wind limit
Rain and link loss | IPX6 propulsion, sealed bay, 4G backup, auto return
Standby power fault | Dock health checks; battery check before dispatch
Regulation and ethics
Drone Rules 2021: small category (2-25 kg); Digital Sky registration, no-permission-no-takeoff, geofence
BVLOS approval needed before real use
No camera recording; minimal data kept
Operator confirms every dispatch
Notes: [4:20-4:40] Main risks and fixes: thin time margin, gusts, rain and link loss, standby power faults. Regulation: under 25 kg is the small category under the Drone Rules 2021, with registration and BVLOS approval needed. Ethics: privacy by design and a human confirms every dispatch.

## Slide 12: References
1. Hobbywing, XRotor X6 Plus datasheet: hobbywing.com/en/products/xrotor-x6-plus269
2. Leishman, J.G., Principles of Helicopter Aerodynamics, 2nd ed., Cambridge Univ. Press, 2006
3. PX4 Autopilot User Guide, uXRCE-DDS bridge: docs.px4.io
4. ArduPilot docs, Hobbywing DroneCAN ESC: ardupilot.org/copter/docs/common-hobbywing-dronecan-esc.html
5. Ministry of Civil Aviation, India, Drone Rules, 2021 (as amended)
6. American Heart Association, resuscitation guidelines (time to defibrillation)
7. Team PHSS sizing script (momentum theory), included in the submission package
All numbers are analytical estimates, not flight-tested. AI assistance used for drafting and the sizing script; declared in Annexure C.
Notes: Reference slide: skip when presenting, keep for Q&A.

## Slide 13: Thank you.
Team 04 PHSS
Saarang A Nair · Harsharaj R
Pramodh Bala T · Sonit Nooney
Notes: [4:40-5:00] Close: the design meets the brief on paper with a hexacopter and zero-preflight standby. Invite questions.